IWGADTS Minutes

April 5th, 2007

NCAR Jeffco Facility

Introduction:

With new attendees, Chris through up a couple introduction slides (Purpose & Areas of Common Interest previously cooked up).  See Chris' slides.  Some word smithing was performed on the “Purpose” slide, and decided that it would be shown at the beginning of every meeting.  The contents of this slide was also put on the front page of the web-site.

Trivial Data Feed Revisit:

Altitude – Decided to add a WGS84 Altitude parameter and rename GPS_alt to

GPS_MSL_Alt.

Time stamp – accept any ISO 8601 format which includes year & month & day & hour &

minute & second.

Future meetings:

Next meeting - Instead of picking a date now, we agreed the next meeting would be in the

fall would be good, and I will canvas starting mid-August.

Future topics:

DC8 update.

Have a meeting to discuss Post Flight Products.

Meeting to discuss Sensor Web.

Briefings:

Carl Sorenson from Dryden gave a Reveal Update.  Two new PC104 cards were

introduced: ppt

- Brandywine has a new IRIG/GPS card.  GPS being the new part.

- Dataforth 8b Signal Conditioner Card.

Rose Dominguez from Ames gave a Payload Computer And Telemetry System (PCATS)

brief/update. ppt

We reviewed the action item list.  Chris Webster will attend the ISRSE conference in late June to give talk on IWGADTS.

Chris Jennison re-iterated we need a better acronym than IWGADTS.  Anyone?

Lunch 12:15 – 1:30

Tour GV 1:30 – 2:00

More Briefings:

Larry Freudinger from Dryden gave IEEE-1588 timing briefing, Precision Time Protocol (PTP).  Could provide nano-second accuracy and may soon be integrated into NTP.  Just a state of the art NTP server in a year or two could do the trick.  ppt

Gordon Maclean from NCAR gave GPS Pulse Per Second (PPS) talk. Gordon gets 1/10 millisecond accuracy feeding a PPS signal into an RS232 port, requires some linux hacks.  ppt

Chris Webster briefs on instrument status.  Instruments would broadcast/multicast little web pages, which a server would pick up and make available to anyone with a web browser.  “web-status”. (see example on wiki, RAF Handbook).

User Survey.  Worked on the survey, starting with a question list from Jeff Myers.  It is on the wiki and an Email discussion should ensue shortly.

http://wiki.eol.ucar.edu/iwiki/FacilityRequirementsSurvey

New action items:

5:00 Adjourn.