APPENDIX B.6

RAF PROJECT SAFETY COMMITTEE

HAZARDOUS MATERIALS AND DEVICES

(Page 1 of 4)

DO NOT WRITE IN THIS BLOCK

Project: 		____DC3_________		Installation Period:	Mar 6 – Apr 30 2012

Aircraft: 		____GV _________		Beginning Date: 	__8 May_ 2012_____

Instrument Number:	_________________		Ending Date: 		__30 June 2012_____

1. 	Instrument: 		___GT-CIMS____________

2.	Function: 		__Measurement of Inorganic Acids_______

3.	Principal Investigator:	_____Greg Huey____________

Address: 		__311 Ferst Dr., Atlanta, GA 30332___

Telephone: 		__404-384-9533_____________________

4. 	Instrument Operator(s):  Greg Huey, Robert Stickel, Dexian Chen, Dave Tanner, Andy Neuman, John Nowark

5.	Is this instrument commercially produced? 	_____no________________

6.	If so, please list name and address of manufacturer:

7. 	Please list serial number of the instrument:

_______N/A_______________________________________

Please attach a copy of the manufacturer’s instruction manual for the device.  If this is not possible, attach a copy of those pages of the instruction manual which describe the principles of operation, hazard warnings, safety features, and safety rules.

8. 	If the instrument is not commercially produced, please provide information requested below:

Designed by:

Organization: 	_______________________________________________

Address: 		_________________________________________________

Telephone: 		________________________________________________

Built by: 	            ____________

Organization:         ________________________________________________

Address: 	            _________________________________________________

###### APPENDIX B.6

# RAF PROJECT SAFETY COMMITTEE

HAZARDOUS MATERIALS AND DEVICES

(Page 2 of 4)

9.	Describe principles of operation, hazard warnings, safety features:

The GT-CIMS utilizes chemical ionization to detect trace gases in the atmosphere. Air is pulled through a heated inlet into the CIMS where select molecules are ionized and mass analyzed. The largest safety hazards are high voltage and compressed gases. All high voltages on the CIMS are interlocked so that if the pressure in the instrument is too high the high voltages are disabled. DOT certified cylinders are used for all compressed gases and include regulators with overpressure protection. All heaters are fused and thermally protected.

10. 	If the instrument is commercially produced, has it been modified? 	___________

11. 	If modified, describe the modification.

All investigators please answer the following:

12. 	Does the instrument contain, use, or produce:

Radioactive materials		__X___	Compressed gases		__X___

Other ionizing radiation	______	Non-ionizing radiation	______

Flammable liquids		______	Laser				______

Radar				______	Flammable gases		______

Explosive materials		______	Toxic materials		______

13. 	If any of the categories were checked, specify the material below (for example, amount, energy levels, physical form, etc.).

Radioactive ion source – 210 Polonium 20 milliCuries, physical form solid gold coated foil contained inside metal cylinder that is vacuum sealed.

Compressed gas, UN1956, Nitrogen – 1.5 kg in 8” dia cylinder x 54” tall

Compressed gas, UN1956, Sulfur Hexaflouride (0.1%) balance nitrogen, - 0.2 kg in 4” dia cylinder x 10” tall

Compressed gasUN1956, Sulfur Dioxide (1 ppmv) balance nitrogen, - 0.2 kg in 4” dia cylinder x 10” tall

###### APPENDIX B.6

# RAF PROJECT SAFETY COMMITTEE

HAZARDOUS MATERIALS AND DEVICES

(Page 3 of 4)

14. 	Please list all other chemicals you will use on board this aircraft in your experiment.

15.	If your experiment consumes or discharges materials, will you need to carry additional materials on board?    NO

16. 	 What and how much extra materials will you need to carry?

None besides gas cylinders on plane

17. 	What kind of container will you need to carry these materials?

________________________________________________________________________

18. 	If the device utilizes a laser, please classify the laser according to ANSI Z 136.1-1973 (circle one).

Class:	I     II     III     IV

- If your laser will be operating at a wavelength that is not eye safe,  what procedures will

be established to minimize the danger to yourself and other project participants?

______please attached a separate document covering this question__________________

20.	If you are using compressed gas cylinders, what is the maximum pressure expected for each cylinder type?

___2000 psig________________________

21.	Will you be re-filling any compressed gas cylinders yourself, either at JeffCO or during the field deployment?

______yes – probably once____________________________________

22. 	Are there any other hazards associated with the instrument itself, the required ground support equipment or the experiment which have not so far been covered in this questionnaire?

23. 	How would you describe the probability of an accident resulting from the presence and use of your instrument on board the NCAR aircraft?

Low – probably largest hazard is heaters but they are all fused, and thermally protected.

###### APPENDIX B.6

RAF PROJECT SAFETY COMMITTEE

HAZARDOUS MATERIALS AND DEVICES

(Page 4 of 4)

24.	How would you describe the severity of such an accident?

Low all heated parts are non-combustible and certified for HIAPER.

25. 	What precautions will you take to decrease the probability and the severity of an accident?  If any documented safety procedures from your home facility or university are available, please attach a copy of said materials to this form.

A checklist of instrument parameters will be established and reviewed before each flight so that the instrument is within specifications.

____4/21/2012		________________________________________________

Date				  Signature of principal investigator or operator

_____Greg Huey_______________

Printed name of principal investigator or operator

________________________________________________

Reviewed by

________________________________________________

Date