## Slide 1
Wave Estimates From ScanSAR Data:
Old Problems, New Solutions
Roland Romeiser
University of Miami, RSMAS-AMP & CSTARS rromeiser@rsmas.miami.edu
ROMEISER ET AL. WAVES FROM SCANSAR ITOP SANTA FE 2011
ROMEISER ET AL. WAVES FROM SCANSAR ITOP SANTA FE 2011
and the ITOP SAR Team
C. Wackerman (GD-AIS), M. Caruso & H. Graber (CSTARS), J. Horstmann (NURC), D. Walker (SRI), R. Foster (UW-APL)

## Slide 2
ScanSAR vs. Stripmap SAR
100 km
450 km
  
  
  
   Much better coverage, scanning over multiple adjacent sub-swaths
   Reduced spatial resolution (100 m vs. 25 m at C band)
   Sub-swath switching may cause specific ScanSAR imaging artifacts

## Slide 3
ScanSAR Imaging Artifact: Scalloping
RADARSAT-1 ScanSAR image of hurricane Helene (2006), 450 km × 1240 km
Two subsections of 1024 × 1024 pixels = 51.2 km × 51.2 km
  
  
  
  
   Wave-like periodic intensity modulation artifact
   Found in many ScanSAR images of ocean scenes from various satellites and SAR processors
   Big problem for wave and wind retrievals
   Post-processing filter developed in ITOP

## Slide 4
ScanSAR Imaging Artifact: Beam Seams
ScanSAR image of hurricane Katrina (2005)
  
  
   Some ScanSAR images exhibit visible beam seams and / or bright "nadir ambiguity" line
   GD-AIS developed specific filter to remove such artifacts

## Slide 5
  
  
  
  
  
SAR Imaging of Ocean Waves
   Tilt modulation of incidence angle
   Hydrodynamic modulation of small-scale roughness
   Nonlinear SAR imaging artifacts ("velocity bunching")
   Modulation strengths vary with wavelength and direction, as well as with wind vector, local incidence angle, etc.
   Conversion of image spectrum to ocean wave spectrum is challenging task, even more under typhoon conditions

## Slide 6
MTF-Based Wave Retrieval Algorithm
SAR Image Intensity Array
Fourier Transform
Image Spectra
Peak Wavelengths, Directions, SWHs
Modulation Transfer Function
Ocean Wave Spectra
Analysis
  
  
   Idea: Empirical algorithm could account for neglected effects, lead to improvements without complex theoretical modeling
   Wind algorithms have always used empirical functions
  
  
  
  
   Neglects nonlinearities of imaging mechanism
   Neglects wavelengths below spatial resolution
   Neglects specific high sea state effects
   Requires detectable wave signatures to work

## Slide 7
New Empirical Wave Retrieval Algorithm
SAR Image Intensity Array
Fourier Transform & Filters
Image Spectra
Ocean Peak Wavelengths
Peak Analysis Routine
Image Peak Wavelengths
Image Peak Directions
Empirical Relation
Ocean Peak Directions
Empirical Relation
Ocean SWHs
Image Mean Intensities
Averaging
  
  
  
   Developed using RADARSAT-1 hurricane images and WAM spectra
   SWH depends most strongly on mean intensity & peak direction
   Extrapolated peak directions permit SWH estimates everywhere; no wave signatures required!

## Slide 8
Example Result: Megi 2010-10-15 21:01 GMT
RADARSAT-2 Image
  
  
   Peak wavelength & direction: Similar results; differences partly due to different filtering & peak detection methods
   SWH: Better coverage with new method; large values around center of storm consistent with SWAN

## Slide 9
Example Result: Megi 2010-10-17 21:44 GMT
RADARSAT-2 Image

## Slide 10
  
  
  
  
  
  
  
Summary & Outlook
   New scalloping and beam seam filters enable routine use of ScanSAR imagery for wave and wind retrievals
   MTF-based wave retrieval works (see Wackerman), but limited spatial coverage, seems to underestimate SWH
   New empirical wave retrieval algorithm estimates wave parameters from properties of image and image spectrum
   Similar to wind retrieval with empirical model function
   Can account for effects of sub-resolution-scale waves and nonlinearities implicitly
   Can estimate SWH where no wave signatures exist
   Upcoming: Detailed comparisons, further refinement, combination of the two wave algorithms, combination of wave and wind algorithms

## Slide 11
END OF PRESENTATION
rromeiser@rsmas.miami.edu