9/15/11

Aircraft Research Instrumentation

C-130 - Basic RAF ICE-T Configuration

Heymsfield et al

RAF-Supplied Instrumentation:

I.  Airborne Data System.

A. Acquisition.  C-130 NIDAS. NCAR Distributed Sampling

Modules (7 units).

B. Operator Station. Intel L440GX+ Motherboard with

2 Pentium III-500 CPU’s, 512 MB Memory, Redhat

Linux 6.2 OS.  9GB Disk Storage with RAID-1.

General Digital 17 inch 1280x1024 TFT Flat Panel

Color Monitor.  IBM-DRHS36D 36GB Removable Disk Drives

In Kingston Carriers (2 units). UPS.

II. Aircraft Position, Velocity and Attitude

A. Honeywell Model HG1095-AC03 Laseref SM Inertial

Reference System . (Research).

B. Garmin GPS16 Global Positioning System. (GPS).

C. NovAtel Model OEM 4 L1/L2 Differential GPS High Accuracy

Positioning System (DGPS)

III. Static Pressures.

A. Paroscientific Model 1000 Digital Pressure Transducer -

Fuselage Port (PSFD).

B. Paroscientific Model 1000 Digital Pressure Transducer -

Fuselage Port (PSFRD, PSFC).

C. Rosemount Model 1201F1 Pressure Transducer –Cabin (PCAB).

D. Rosemount Model 1201F1 Pressure Transducer –CN Counter (PCN).

IV. Dynamic Pressures.

A. Rosemount Model 1221F1VL - Radome (QCR).

B. Rosemount Model 1221F1VL – Left Fuselage Pitot (QCF).

C. Rosemount Model 1221F1VL – Right Fuselage Pitot (QCFR).

V.  Temperatures.

A. Rosemount Type 102 Non-deiced Sensor -- Rosemount Model

510BF Amplifier - Port Radome Mount (TTRL).

B. HARCO Deiced Sensor -- Rosemount Model

510BF Amplifier - Left Fuselage (TTHR1, TTHR2).

D. OPHIR3 Radiometric Temperature Sensor – Right Wing Pod (OAT).

VI. Flow Angle Sensors, Radome.

A. Attack - Rosemount Model 1221F1VL Differential Pressure

Transducer (ADIFR).

B. Sideslip - Rosemount Model 1221F1VL Differential

Pressure Transducer (BDIFR).

C-130 RAF ICE-T

Page 2

VII. Dew Point and Humidity.

A. Buck Research, Model 1011C Dew Point Hygrometer –

Starboard Radome Mount (DPT).

B. Buck Research, Model 1011C Dew Point Hygrometer - 	    	   	   Starboard Radome Mount (DPB).

C. TDL Laser Hygrometer – Right Wing Pod.

D. RAF Fast Response UV Hygrometer – L3 aperture (XUVI)

VIII.   Radiometric Sensors.

A. Remote Surface Temperature.  Heiman Model KT19.85

Radiometer - 2 units: Down looking (RSTB,RSTB1).

B. Remote Sky Temperature.  Heiman Model KT19.85 Radiometer.

Up looking (RSTT).

IX. Wing Stores

A. RAF - Particle Measuring Systems Model SPP-100

Size Distribution, 3 - 45 um. LWO.

B. RAF - Modified PMS 2D-C Optical array Probe

Size Distribution, 25 to 1600 um. LPO.

C. RAF – Modified PMS 2D-P Optical Array Probe

Size Distribution, 150 to 8100 um. RPO.

- RAF – SPEC – 3V-CPI Particle Imager. RPI.

Size Distribution, 25 to 800 um.

E. RAF - Particle Measuring Systems Model SPP-200

Size Distribution, 0.1 - 3 um. RWO.

F. RAF - Particle Measuring Systems Model SPP-300

Size Distribution, 0.3 - 20 um. LPC.

- DMT – CDP Cloud Droplet Probe

Size Distribution, 3 - 45 um. LWI.

- SID-2H – EOL Small Ice Detector. RWI.

- HOLODEC 2 – Holographic Particle Imager. LPI.

X.  Basic Cloud Physics.

A. PMS Liquid Water Sensor (King Probe) -

Left Outboard Wing Access Plate (PLWC).

B. TSI Model 3760 CN Counter - Belly Inlet (CONCN).

Size Distribution, 0.01 to 3 um.

C. Rosemount Icing Rate Indicator

Right Outboard Wing Access Plate (RICE).

XI. Photography.

- Forward Looking Digital.

- Down Looking Digital.

C-130 RAF ICE-T

Page 3

XIII. RAF Chemistry (T.Campos).

- EOL Fast Ozone (FO3_ACD).

- EOL Picarro Carbon Dioxide (CO2_PIC).

- EOL Picarro Methane (CH4_PIC).

- EOL Carbone Monoxide.

XIV. Special Request Cabin Mounted Instrumentation.

A. Wyoming mm Cloud Radar – up & down looking options.

- Wyoming Cloud Lidar – up looking / Fwd Top Fuselage Aperture.

- Wyoming Cloud Lidar – down looking / large belly

- Clarkson CN Inlets (3), CCN Counter, CN counters (3)

- DRI CN Counters (2 units).

- DMT SP2 Black Carbon Sensor.

- CSU CFDC Ice Nuclei Counter.

- DMT ASPD Aerosol Particle Sizing System.

- UCSD Real time AMS Particle Analyzer.

- ASU Aerosol Filter packs.

- Univ of Frankfort FRIDGE Filter Pack System.

- EOL Counter-flow Virtual Impactor (CVI).

- CU Picarro Isotopic Water Analyzer